## Slide 1
Project Presentation of CO-OP Project at Industry (Module-2) (22CS421)
On
Artificial Intelligence for Real-Time ECG Analysis and Smart Cardiac Monitoring
Shubham Guglani
2210990846
Submitted To
Dr. Preeti Saini
Department of Computer Science and Engineering,
Chitkara University, Punjab

## Slide 2
Introduction
2
Cardiovascular diseases (CVDs) are the leading cause of mortality worldwide, requiring continuous round-the-clock monitoring.
Traditional ECG monitoring relies on manual interpretation or rigid rule-based systems that frequently miss sporadic or early-stage arrhythmias.
Paroxysmal Atrial Fibrillation (AF) — a major stroke risk factor — is often missed by brief periodic clinical snapshots.
Artificial Intelligence (AI), specifically deep learning, has transformed ECG analysis by enabling automated beat-to-beat interpretation with superior accuracy.
This research focuses on software-centric AI architecture: pivoting from VLSI hardware designs to high-level algorithmic efficiency and cloud-native stacks.
Key objective: Build a scalable, real-time ECG classification and arrhythmia detection framework achieving >98% accuracy with sub-millisecond latency.

## Slide 3
Problem Statement
3
The Deployment Dilemma: Deep learning models contain millions of parameters, demanding heavy compute — incompatible with wearable constraints.
Wearable devices require: power budgets in microwatts, inference latency under 1 ms, and minimal chip/memory footprint.
Rule-based systems fail to generalize across diverse patient populations or noisy ambulatory environments.
Class imbalance in training data: normal heartbeats vastly outnumber arrhythmic ones, reducing model sensitivity.
Transformer models offer high accuracy but have O(n^2) complexity — computationally prohibitive without optimization.
Challenge: Balance diagnostic accuracy (>98%) with real-time feasibility and edge deployability.

## Slide 4
Literature Review
4
2015-2018: SVMs and decision trees used with expert-defined features (QRS width, P-wave duration). Limited by heuristic dependence.
2018: 1D CNNs revolutionized feature extraction — automating morphological pattern detection, achieving 96.44% accuracy.
2023: Hybrid CNN-BiLSTM architectures became state-of-the-art, combining spatial and temporal modeling — ~99% accuracy on MIT-BIH database.
2024: Depthwise Separable Convolutions (DSC) reduced model footprint; Transformer models enabled global ECG context awareness.
2024-2025: Spiking Neural Networks (SNNs) — event-driven, asynchronous — achieved 98.26% accuracy with minimal CPU consumption.
Key benchmark datasets: MIT-BIH Arrhythmia Database (48 recordings), PTB-XL Dataset (21,837 recordings from 18,885 patients).

## Slide 5
AI Model Architecture Comparison
5
Classic SVM: Expert-defined features, O(features) complexity — limited to clear, predefined anomalies.
1D CNN: Automated morphology extraction, O(n) time complexity — high accuracy for morphological arrhythmias.
LSTM: Temporal dynamics modeling, O(n) time, O(hidden size) space — ideal for long-term rhythm-based disorders.
Transformer: Global context attention, O(n^2) time and space — highest accuracy but critical latency impact.
Event-Driven SNN: Asynchronous spike processing, O(spikes) time, O(neurons) space — negligible latency, ideal for edge.
Best choice for real-time: Hybrid CNN-BiLSTM (linear O(n) complexity) or optimized SNN for ultra-low-power wearables.

## Slide 6
Software Architecture & System Integration
6
Layer 1 — Ingestion: Millions of heart monitors connect via MQTT/WebSockets; FastAPI gateway handles routing with minimal overhead.
Layer 2 — Message Broker: Apache Kafka decouples ingestion from processing; topics partitioned for parallel consumption by worker pods.
Layer 3 — Data Processing: Containerized SciPy/BioSPPy services perform denoising, baseline correction, and R-peak detection.
Layer 4 — Inference: NVIDIA Triton Inference Server with dynamic batching and concurrent model execution for GPU efficiency.
Layer 5 — Application: Clinician dashboard with real-time alerts; EHR interoperability via FHIR standards.
Kubernetes HPA auto-scales pods beyond 60% CPU/memory threshold; Go-based microservices yield 6-10x compute efficiency vs. monolithic.

## Slide 7
Data Processing Pipeline
7
Band-pass Filtering: 4th-order Butterworth filter eliminates baseline wander and high-frequency noise; FFT-based for O(n log n) efficiency.
Normalization: Min-max or Z-score scaling maps amplitudes to [-1, 1], ensuring optimal neural network activation.
R-Peak Detection: Pan-Tompkins algorithm identifies QRS R-peaks; signal segmented into heartbeats (180-250 sample windows).
Data Augmentation: GANs and Time-VQVAE generate synthetic arrhythmic heartbeats to address class imbalance.
Patient-independent partitioning: No patient data shared between training and test sets — prevents overfitting.
Tools: SciPy/BioSPPy (denoising), Py-ECGDetectors (R-peaks), NumPy (segmentation), Scikit-learn (normalization).

## Slide 8
Experimental Setup & Results
8
Environment: Python 3.10+, TensorFlow 2.18, PyTorch — trained on server-grade GPUs within a local Kubernetes cluster.
Datasets: MIT-BIH Arrhythmia Database, PTB-XL (21,837 recordings), Synthetic Augmented Dataset (Time-VQVAE).
Hybrid CNN-BiLSTM achieved 98.22% accuracy on multi-class detection; standalone CNN: 90.93% (confirms temporal context is vital).
CNN-Transformer architecture reached 99.71% accuracy — highest diagnostic performance, but with significant latency trade-off.
System latency: Median 22ms per request (FastAPI-Triton); throughput of 780 requests/second under 1,000 concurrent streams.
Tail latency P95 under 100ms confirms cloud-native orchestration supports mission-critical monitoring at scale.

## Slide 9
Algorithmic Complexity & Model Compression
9
1D CNN: O(n) time, O(weights) space — linear, GPU-parallelizable; ideal for morphological detection.
LSTM: O(n) time but sequential gate computation limits parallelization — higher CPU latency than CNN.
Transformer Self-Attention: O(n^2) time and space — prohibitive for long ECG recordings without kernel-level optimization.
Precision Quantization: FP32 to INT8 conversion reduces memory footprint by 75%; accelerates inference on standard CPUs.
Weight Pruning: Removing near-zero neurons achieves 80% sparsity — requires sparse-matrix libraries for actual gains.
Combined INT8 quantization + pruning enables deployment of advanced AI models on mobile/wearable hardware.

## Slide 10
Conclusion & Future Directions
10
Hybrid CNN-BiLSTM models with O(n) linear complexity deliver cardiology-level accuracy (98.22%) with sub-second latency in cloud-native stacks.
INT8 quantization and weight pruning are the primary enablers for deploying advanced AI on resource-constrained wearable devices.
Event-driven Kafka + Kubernetes architecture provides horizontal scalability from single wearables to enterprise clinical environments.
Future 1 — Federated Learning: Decentralized training adapts models to individual patients without transferring sensitive biometric data.
Future 2 — Multimodal Fusion: Combining ECG with PPG and motion data to build a patient digital twin for accurate risk stratification.
Future 3 — Foundation Models: Pre-training large encoders (HuBERT-ECG) on millions of records to discover new subclinical digital biomarkers.

## Slide 11
Thank You
3